## Slide 1: Beam Cooling

## Slide 2: Beam Temperature
We define the beam temperature as:
  The longitudinal temperature:
  The transverse temperature
Notes: \frac{1}{2}kT_\parallel=\frac{1}{2}mv_\parallel^2=\frac{1}{2}m \beta^2 c^2\left(\frac{dp}{p}\right)^2

## Slide 3: Why beam is hot
The beam is generated at source. They have temperature from the distribution
  Electron come from cathodes, with initial Fermi-Dirac distribution
  Proton come from the plasma, with Maxwell-Boltzmann distribution
Later on the beam can be ‘heated’ due to mismatch, intra-beam scattering, residue gas, etc.

## Slide 4: What is beam cooling
Cooling is to reduce the phase space area of the beam or the temperature of the beam, or maintain the emittance against the factors to make emittance growth.
We already learn ways to reduce emittance which are not cooling methods:
  Acceleration
  Collimation

## Slide 5: Way of Cooling
Synchrotron Radiation
Ionization Cooling
Electron Cooling
Stochastic Cooling
Coherent electron cooling

## Slide 6: Electron does not need cooling:
Synchrotron Radiation is a natural way of cooling (damping).
Revisit the energy deviation motion:

## Slide 7: Synchrotron Radiation
With the damping force that is proportional to the velocity, this is not a Hamiltonian system anymore.
SR is also bring large heating effect and balance out its damping effect, as we learned earlier.
Notes: \Delta E\sim \exp{\left(\pm\sqrt{\alpha_E^2-\omega^2}-\alpha_E\right)t}

## Slide 8: Electron Cooling
Cold electron interact with hot ion beam via Coulomb interaction.
Longitudinal temperature: ~1e-4eV
Transverse temperature:~0.1eV
G. Budker

## Slide 9: Electron Cooling II
In the electron beam velocity reference frame:
E-beam
E-beam
Faster ions
Slower ions
Maximum cooling force
For small relative velocity
For large relative velocity

## Slide 10: Electron Cooling III
The cooling time:
Therefore the electron cooling is good for:
  Cold beam
  Low energy beam
  Dense electron beam
  Highly charge beam
Does not matter on the intensity of the ion beam.

## Slide 11: Electron Cooling IV
Electron is usually confined in longitudinal magnetic field. (Magnetized cooling)
All electrons experience cyclotron motion.
Interaction time >> cyclotron period, the transverse temperature is not important, only depend on longitudinal temperature.

## Slide 12: Electron Cooling Example: LEReC @ BNL
First demonstration of electron cooling using RF accelerated electron beam.
For the low-energy RHIC run for searching QCD critical point.
Long proton (~30 ns) vs. short electron, RF frequency 704 MHz.
  Solution: Micro bunch trains.

## Slide 13: E-Cooling: LEReC, bunch trains
30 ‘micro’ electron bunch trains for one proton bunch.
@ A. Fedotov
 | Ion | Electron
Bunch charge | 5e8 Ions | 6.3e8 (100pC)
Bunch length | ~3m | ~3cm

## Slide 14: E-Cooling: LEReC, setup
@ A. Fedotov

## Slide 15: E-Cooling: LEReC, Observation
Electron and ion are well matched.
Bunch being cooled.
Witness bunch
@ A. Fedotov

## Slide 16: Ionization Cooling
Muon collider needs much shorter cooing time, since they decay in 2.2 micro seconds.

## Slide 17: Ionization Cooling II
As we noticed, this is naturally a transverse process, we can use dispersive region to make it also work in longitudinal plane.

## Slide 18: Stochastic cooling
First brought up and realized in CERN by Simon van der Veer.
Nobel Laureate.
A negative feedback system for individual particles’ signal.
(N+0.5) pi phase advance between pickup and kicker

## Slide 19: For individual particle

## Slide 20: Bandwidth Rules
Requires infinite bandwidth
For a finite bandwidth W, the signal is averaged in time window of 1/2W.

## Slide 21: Mixing
Without cooling, the cooling process will stop after the first iteration.
Good mixing:
kicker to pickup
Bad mixing:
pickup to kicker

## Slide 22: Stochastic Cooling at RHIC
Kicker Cavity

## Slide 23: Bandwidth Improvement Coherent Electron Cooling
Modulator
Kicker
Dispersion section
( for hadrons)
Electrons
Hadrons
l2
l1
High gain FEL (for electrons)
Eh
E < Eh
E > Eh
Eh
E < Eh
E > Eh

i
vi
ve
Bandwidth determined by FEL, also good fore high energy

## Slide 24: CEC II