## Slide 1: Synchrotron Light Source

## Slide 2: Radiation Spectrum

## Slide 3: Wavelength and Photon Energy
The following relations are readily used:
1 angstrom hard x-ray, energy is 12.4keV
Visible light 500nm, energy is 2.4 eV

## Slide 4: SR Light Source Worldwide
Source: Lightsources.org

## Slide 5: SR Light Source Worldwide
ESRF, 6 GeV
SSRF, 3.5 GeV
NSLS II, 3 GeV
SPring-8, 8 GeV

## Slide 6: Example Lattice APS - DBA
Parameters | value
Energy | 7 GeV
C | 1104 m
Ns | 40
eps | 8.22 nm rad
Qx | 35.22
Qy | 14.30
alpha | 2.28e-4
APS @ ANL
APS-U project upgrade the lattice to MBA

## Slide 7: Example Lattice NSLS II - DBA
Parameters | value
Energy | 3 GeV
C | 781.0 m
Ns | 15
eps | 2.03 nm rad
Qx | 32.34
Qy | 16.28
alpha | 3.67e-4
NSLS-II @ BNL

## Slide 8: Example Lattice: ESRF - DBA
Parameters | value
Energy | 6 GeV
C | 844 m
Ns | 32
eps | 4.0 nm rad
Qx | 36.44
Qy | 13.39
alpha | 1.78e-4
ESRF @ France
Old DBA lattice

## Slide 9: Example Lattice: ALS - TBA
Parameters | value
Energy | 6 GeV
C | 844 m
Ns | 32
eps | 0.134 nm rad
Qx | 76.21
Qy | 27.34
alpha | 8.4e-5
ALS @ LBNL
ALS-U project upgrade the lattice to MBA

## Slide 10: Example Lattice: MAX-IV - 7BA
Parameters | value
Energy | 3 GeV
C | 528 m
Ns | 20
eps | 0.33 nm rad
Qx | 42.24
Qy | 16.28
alpha | 3.07e-4
MAX-IV @ Sweden

## Slide 11: SR Light Source
To produce UV, (soft/hard) X-ray source
  Dipole, undulator/wiggler
EXCITING SCIENTIFIC TOOL.
LET LIGHT MEET MATTERS

## Slide 12: Performance of light source
Brightness of photon
Flux
Notes: B=\frac{d^4N}{dtd\Omega dS(d\lambda/\lambda)}

## Slide 13: Higher Brightness Enable Us…
Process with less cross section
Trim the light for better
  Coherence, monochromatic radiation
Protein Crystallography
Spectroscopy with high resolution
Crystal Diffraction
Many More…

## Slide 14: SR is polarized light

## Slide 15: SR from Bending Magnet
Goods
  Simple, inexpensive
  Broad spectral range
  Many beamlines
Bads
  Limited hard x-ray components
  Not very bright

## Slide 16: SR spectrum of Dipole, Energy Dependence

## Slide 17: Undulator/Wiggler
In addition to the SR from dipoles, modern light sources has many long straight section with zero dispersion function.
They are undulators and wigglers with similar shape but different parameter.
Example: NSLS II
# of DBA cells: 30
# of 5m straights: 15
# of 8m straights: 15

## Slide 18: Real Example

## Slide 19: SR from Undulator/Wiggler
They are ‘insertion devices’ in straight sections. Modern accelerators provides many long straight sections.

## Slide 20: Difference between bending magnet and Undulator/Wiggler
Courtesy of W. Barletta

## Slide 21: Brightness Comparison
Courtesy of W. Barletta

## Slide 22: Electron Motion inside Undulator
Notes: B=B_y=B_0\cos\frac{2\pi z}{\lambda_u}
\frac{dP_x}{dt}=ecB_0\cos\frac{2\pi z}{\lambda_u}
v_x=\frac{eB_0\lambda_u}{2\pi m\gamma}\sin\frac{2\pi z}{\lambda_u}\equiv\frac{Kc}{\gamma}\sin\frac{2\pi z}{\lambda_u}
K=\frac{eB_0\lambda_u}{2\pi mc}=0.934B_0[T]\lambda_u[cm]

## Slide 23: Undulator ‘Slows down’ the electron
oscillating part is averaging to zero
As if the energy of beam changes:
Notes: v_z=\sqrt{v^2-v_x^2}=c\sqrt{1-\frac{1}{\gamma^2}-\frac{K^2}{\gamma^2}\sin^2\frac{2\pi z}{\lambda_u}}
=c(1-\frac{1+K^2/2}{2\gamma^2}+\frac{K^2}{4\gamma^2}\cos\frac{4\pi z}{\lambda_u})

## Slide 24: In electron ‘s rest frame
The electron sees contracted undulator
The frequency of the radiation is
In lab frame, the frequency of the radiation is different(relativistic Doppler Effect)
Notes: f=\frac{f^\prime}{\gamma^*(1-\bar{\beta_z}\cos{\theta})}=\frac{c}{\lambda_u(1-\bar{\beta_z}\cos{\theta})}

## Slide 25: Resonance Condition
The wavelength of the radiation in the lab frame:
Recall that:
And we only care of small forwarding angle:
Finally the wavelength reads:

## Slide 26: Radiation for K<1
Radiation Bandwidth:
Angle for central cone
Power:
Courtesy of W. Barletta

## Slide 27: Wiggler Radiation
When K>>1, the high harmonics become important and very dense.
The envelope is similar to the SR from dipoles. The brightness is increased by 2N

## Slide 28: Beamline 101